## Slide 1: Mechanistic study of CAL-B catalyzed ring-opening polymerization of β-lactam: First results of the hybrid MC/MD simulation study
Chantal Barberot, Ikuo Kurisaki, Yuichi Suzuki, Masataka Nagaoka
Nagaoka Laboratory, Graduate School of Information Science, Nagoya University

## Slide 2: Polyamides
monomer unit
Nylon 3, poly(β-alanine)
Polyamides are one of the most used polymers, found in several applications in industry, e.g., plastics, fibers.
Among polyamides, nylon 3 is composed of a β-alanine monomeric unit and is widely used in industry .e.g.;
  the manufacturing of nano-composites [1]
  cosmetic [2]
  water purification [3]
[1] Itagaki, T.; Komori, Y.; Sugahara, Y.; Kuroda, K. J. Mater. Chem. 2001, 11, 3291–3295.
[2] Grollier, J. F.; Fourcadier, C.; Courtois, M. Detergent and foaming cosmetic composition delaying the regreasing of hair. US4851154, 1989.
[3] Huang, S. Y.; Fisher, M. M. Water purification employing poly(beta-alanine). US4247432, 1981.
Nylon 6, 6
Nylon 6 or PA6

## Slide 3: Poly(β-alanine) synthesis
There are several ways to synthesize poly(β-alanine)
  Anionic polymerization of acrylamide in the presence of a strong base [4].
  Polymerization through group (IV) metal alkoxides [5].
  Polycondensation of β–alanine in ionic liquid [6].
  Enzymatic polymerization [7].
In order to apply this strategy for an industrial use, it seems important to optimize the reaction conditions or improve the enzymatic function of the CAL-B itself.
 | Reactant | Catalyzer | Yield (%) | DP | DPmax
Entry 1 | acrylamide | t-Butyl-ONa | 65% |  | 
Entry 2 | β-alanine | No catalyzer | 74 | 10 | 24
 |  | Metal alkoxides = Zr(Ot-Butyl)4 | 81 | 15 | 53
 |  | Metal alkoxides = Hf(Ot-Butyl)4 | 75 | 24 | 58
Entry 3 | β-alanine | Ionic liquid = [MMlm]Cl | 83 | 49.5 | 
 |  | Ionic liquid =[MMlm](MeO)2PO2 | 94 | 27.8 | 
Entry 4 | β-lactam | CAL-B | 73 | 8 | 18
[4] Breslow, D. S.; Hulse, G. E.; Matlack, A. S. J. Am. Chem. Soc. 1957, 79, 3760–3763.
[5] Steunenberg, P.; Könst, P. M.; Scott, E. L.; Franssen, M. C. R.; Zuilhof, H.; Sanders, J. P. M. Eur. Polym. J. 2013, 49, 1773–1781.
[6] Zhang, S.; Dias Goncalves, L.; Lefebvre, H.; Tessier, M.; Rousseau, B.; Fradet, A. ACS Macro Lett. 2012, 1, 1079–1082.
[7] K. Loos et al. Macromol Rapid. Commun. 2008, 29, 794-797.
It can lead to branched polymer
It is not environmental friendly reaction conditions

## Slide 4: Research project
To optimize the reaction, a deep understanding of the mechanism is necessary.
Currently, a mechanism was already proposed [8]. Unfortunately, no reaction energies were given.
  The rate-determining step of the reaction is still elusive
As a first step to produce longer Nylon 3 polymer, we investigated the mechanism of the polymerization reaction with QM and QM/MM calculations.
During a second stage, we will perform hybrid MC/MD simulations [9] to consider the effects of the system dynamic on our proposed mechanism.
[8] G. Fels et al. ACS Catal. 2011, 1, 323-336.
[9] Nagaoka, M.; Suzuki, Y.; Okamoto, T.; Takenaka, N. Chem. Phys. Lett. 2013, 583, 80–86.

## Slide 5: QM and QM/MM studies

## Slide 6: Methodology
1. System description
  Crystal structure: 4K6G
  Solvent: 2770 toluene molecules + 92 water molecules
2. Procedure
Force field parameters:
  Organic molecules: general AMBER force field
  Protein: Amber force field ff99SB
  Water molecules: TIP3P model
  Na+: JC ion parameters
QM Calculation level: B3LYP/6-31G(d,p)
[10] Nagaoka, M.; et al. J. Comput. Chem. 2011, 32 (5), 932–942. Nagaoka, M.; et al. Bull. Chem. Soc. Jpn. 2013, 86 (2), 210–222.
MD
pick-up a snapshot structure and minimized by MM
extract the active site
QM calculations in gas phase with Gaussian
QM/MM calculations with Amber Gaussian interface (AG-IF) [10]
•
active site
105Ser
106Gln
41Thr
188Asp
224His
104Trp
40Gly
42Gly
225Ala
223Asp
Oxyanion hole
Catalytic triad
Model system and QM part

## Slide 7: Results and Conclusion
The initiation process is not performed through the in situ β–lactam opening.
Water molecules should play two roles in the polymerization reaction.
Linear condensation process seems is the rate-determining step.
not favorable
polymer release
Reaction initiation
Monomer activation
Termination
21.71
[kcal/mol]
15.23 [kcal/mol]
33.70 [kcal/mol]
Elongation
19.82
[kcal/mol]
Initiation
path A
path B
41.56 [kcal/mol]
19.82
[kcal/mol]

## Slide 8: MC/MD simulations

## Slide 9: Computational details
The acylated CAL-B is solvated in a toluene box.
92 water molecules are added to the system corresponding to an enzyme water content of 1 % (w/w).
The β-lactam concentration corresponds to the experimental one (0.285 mol.L-1), 92 β-lactam molecules.
Periodic boundaries conditions are applied.
SHAKE method is used to constrain bond involving hydrogen atoms.
To equilibrate the system, a series of MD are performed at 363K and 1 atm.
First, 2000 MC/MD cycles are performed
The NVT-MD (363K) simulation time in one MC/MD cycle is set to 10 ps.
Force field parameters:
  Organic molecules: general AMBER force field
  Protein: Amber force field ff99SB
  Water molecules: TIP3P model
  Na+: JC ion parameters
76 Å
82 Å
96 Å
Acylated 105Ser
Water
β-lactam
Toluene

## Slide 10: Reaction scheme
The chemical reactions are selected based on the distance criteria and their activation energy.
Ligand binding should occur less often than chemical reaction. A correct parametrization is necessary.
In addition, analysis of active site is important to decided if the ligand binding can occur or not.
Monomer activation
Elongation
Termination
Initiation
Ligand
binding

## Slide 11: Docking reaction selection
Docking reaction weight << chemical reaction weight
No β–lactam present in the active site?
Catalytic serine acylated?
Docking reaction weight=0
yes
yes
no
no
Current cycle - last accepted docking cycle
< i cycles
yes
no
Before the reaction selection, a reaction weight is given for the docking process depending of few criteria.
But the selection condition for docking process is more often satisfy that for chemical reaction.
To decrease the probability of selection, another criteria is considered (TRIAL).
First test with i=10 MC/MD cycles and i=20 MC/MD cycles for 4 initial configurations

## Slide 12: β-lactam conversion
The β–lactam conversion corresponds to the percentage of β–lactam which already reacts.
It is calculated at each MC/MD cycle i as follow:
Docking frequency: 10 MC/MD cycles
Docking frequency: 20 MC/MD cycles
After 2000 MC/MD cycles, the maximum conversion observed is only equal to 8.7% was observed.
Some differences can be observed by varying the docking frequency.

## Slide 13: Number of polymer
low conversion
high conversion
Last cycle: 1 monomer
1 dimer
Last cycle: 2 monomers
Docking frequency: 10 MC/MD cycles
Docking frequency: 20 MC/MD cycles
Last cycle: 1 dimer
1 pentamer
Last cycle: 2 monomers
3 dimers

## Slide 14: Number of reactions
high conversion
low conversion
Docking frequency: 10 MC/MD cycles
Docking frequency: 20 MC/MD cycles
1031 MC/MD cycles
834 MC/MD cycles
1823 MC/MD cycles

## Slide 15: Type of accepted reactions
Acylated Serine
Acylated Serine
low conversion
Docking frequency: 10 MC/MD cycles
Docking frequency: 20 MC/MD cycles
Acylated Serine
1
3
4
5
2
Acylation
2

## Slide 16: Type of accepted reactions
high conversion
Docking frequency: 10 MC/MD cycles
Docking frequency: 20 MC/MD cycles
Acylated Serine
Acylated Serine
1
3
4
5
2
2

## Slide 17: Next improvements
The docking process can influence the polymerization results.
  A distance criteria will be used (More realistic).
Docking reaction weight << chemical reaction weight
No β–lactam present in the active site?
Catalytic serine acylated?
Docking reaction weight=0
yes
yes
no
no
β–lactam is
located < d of the active site
Docking reaction can be selected
Docking reaction can not be selected
yes
no
To accelerate the polymerization process simulation, water binding will be also considered.
If the both process is selected at the same type, the probability of selection of each will be weighted by their diffusion constant.

## Slide 18: Elongation process (1)
Based on our electronic state calculation, we showed that the initiation process is performed through path A.
In this case, the oligomer has to be stored in the active site or outside the active site to be used later during the elongation process.
Because of the low diffusion of the oligomer in the solvent media, G. Fels proposed the path B.
not favorable
Monomer activation
Termination
21.71
[kcal/mol]
15.23 [kcal/mol]
33.70 [kcal/mol]
Elongation
19.82
[kcal/mol]
Initiation
path A
path B
41.56 [kcal/mol]
19.82
[kcal/mol]

## Slide 19: Elongation process (2)
The monomer or dimer units can be stored in the active site and be used later for the elongation process.
It is support our proposed mechanism where the oligomer can come from the hydrolysis of the acyl complex.
Dimer formation
Trimer formation

## Slide 20: Conclusion
QM and QM/MM calculations
  A new mechanism was proposed where the initiation reaction occurs thought the acylated complex hydrolysis.
  The elongation process is the rate-determining step of the polymerization reaction. It can explain why only short polymer length are observed experimentally.
MC/MD trial
  A better parametrization for the ligand binding process and add the possibility to simulate the entrance of the water into the active site are necessary.
  The simulation of the elongation process support our proposed mechanism.

## Slide 21: Thank you for your attention